## Slide 1: Introduction to GEBs and GEB Controls
2022 Iowa Energy Summit
Altoona, Iowa
11/09/2022
Xiaohui “Joe” Zhou, PhD, PE, CEM
Director of Research and Innovation

## Slide 2: Who we are
Mission-driven non-profit located in Madison, WI.
Accelerating climate solutions. For everyone.
Nationally recognized technical leadership.
https://slipstreaminc.org/

## Slide 3: Outline
GEB
What is a GEB?
GEB Controls
Three components of a GEB control platform
ADR Through GEB Controls
Automated Demand Response by controlling the HVAC system in a GEB

## Slide 4: GEB

## Slide 5: What is a GEB?
A Grid-interactive Efficient Building (GEB) is an energy-efficient building that uses smart end-use equipment and/or other onsite DERs to provide demand flexibility while co-optimizing for energy cost, grid services, and occupant needs and preferences, in a continuous and integrated way.

## Slide 6: Distributed Energy Resources (DER)
Behind-the-Meter Generation
  Photovoltaics
  Gas-Fired Generation, Combined Heat and Power, Fuel Cells
Energy Storage
  Battery
  Cool Thermal and Refrigeration
Advanced Inverters
Electric Vehicles
Advanced Building Controls

## Slide 7: Why DERs in Buildings
Source: 2019 DOE Grid-interactive Efficient Buildings Overview
+
Modes of Building Load Flexibility

## Slide 8: DER Learning Resource
https://sustainableenergyaction.org/clean-energy-clearinghouse/
A single source to learn about behind-the-meter DERs
Developed by an Interstate Renewable Energy Council (IREC)-led team including Slipstream
Target audience: building managers, operators, and safety officials

## Slide 9: GEB Characteristics
EFFICIENT
Persistent low energy use minimizes demand on grid resources and infrastructure
CONNECTED
Two-way communication with flexible technologies, the grid, and occupants
SMART
Analytics supported by sensors and controls co-optimize efficiency, flexibility, and occupant preferences
FLEXIBLE
Flexible loads and distributed generation/storage can be used to reduce, shift, or modulated energy use
Grid-Interactive Efficient Building Characteristics
Source: DOE, 2019

## Slide 10: GEB Controls

## Slide 11: Different DER Control Models
Integrated
Distributed

## Slide 12: A Generic GEB Control Platform
Integration
  Integrate multiple DERs
  Each subsystem may have its own standards/protocols
Two-way communication
  Receive utility ADR signals
  Respond with feedback info
Optimization and Control
  Brain of a GEB building
  Can optimize DERs based on multiple objectives
    Highest utility incentives
    Minimal carbon impact
    Minimal energy use
    Highest demand reduction
    Acceptable comfort levels
Connected
Flexible
Smart
Connected

## Slide 13: A Generic GEB Control Platform
BAS

## Slide 14: Current GEB Control Software Options
Open-source platform
  Eclipse VOLTTRON
Proprietary, commercial software
  Prescriptive Data - Nantum
  Kinetic Buildings – Synapse
  Others
DERMS (not GEB Control)
  Distributed Energy Resource Management System
  Utility-side control

## Slide 15: Eclipse VOLTTRON
Integration
Communication
Optimization and control
Source: Pacific Northwest National Lab
VOLTTRON
  A Linux-based software platform
  Enables secure coordination of building energy loads and distributed energy resources
  Initially developed by PNNL
  Open-source, publicly available from GitHub

## Slide 16: Slipstream GEB Platform Architecture
HVAC
Meter
Plug Loads
PV
ADR
Aggre-gation
An industrial-grade computer with VOLTTRON installed

## Slide 17: Slipstream GEB Platform Components
Building HVAC Control
BERT Smart Plug
Solar PV Inverter
Computer with VOLTTRON

## Slide 18: Slipstream GEB Platform User Interface
OA Temp
Main Power
PV Power
RTU Power
Grafana
  A web-based visualization tool
  Open source
  Configurable and flexible
  Connected to Slipstream GEB database

## Slide 19: Prescriptive Data - Nantum

## Slide 20: Kinetic Buildings - Synapse
Automated set-up and calibration
During the normal course of a building’s operation, the manner in which each piece of equipment responds to changes is continuously tracked
Setpoint and actuator changes vs. the power and thermal responses
Process
Estimate future demand
Estimate effects of all potential adjustments – bounded by operator
Minimize and distribute impact to occupants
Continuously learn and calibrate
Building automation IP subnet
BAS workstation
Volttron edge node
Router/Switch
Grid/utility data
(multiple protocols)
Weather forecast
Web application
Dashboarding and reporting
Real-time monitoring-based Cx (MBCx)
Configuration of efficiency opportunities and actions
Configuration of demand shedding & shifting actions
Analytics cloud
Database
EMIS platform

## Slide 21: Current GEB Control Software Capabilities
Still mostly only focuses on load reduction through HVAC controls
Need to integrate other DERs
  Lighting & plug loads
  Solar PV and battery storage
  Managed EV charging
Automated Demand Response
  Two-way communications with utilities (OpenADR, IEEE 2030.5)
  Realtime pricing
Optimization and control
  Optimize all DERs
  Multiple objectives
    kWh savings
    kW reduction during peak periods
    kWh and kW $ savings
    Utility incentives
    Carbon emission reduction
    Comfort
  Still mostly in research and testing

## Slide 22: What Knowledge Building Engineers Need to Know
Building automation system
GEB control platform
GEB DER integration
Building-to-grid communication
OT vs IT & cybersecurity
HVAC control strategies for load reduction
How other DERs are operated and maintained
General optimization techniques

## Slide 23: Automated Demand Response Through GEB Controls

## Slide 24: Automated Demand Response Through GEB Controls
Source: LBNL

## Slide 25: Lessons Learned
Issue #1 - zone temperature setpoint deadband too narrow
  More simultaneous heating and cooling
  During load shedding event, the zones can be in heating mode
  Recommend at least 5 deg F
  Adjusting the deadband may be proprietary software tools and done by the building controls contractor
73 Deg F
72 Deg F
Zone Temp
75 Deg F
74 Deg F
Method: Increase zone temperature setpoint by 2 Deg F

## Slide 26: Lessons Learned
Issue # 2 – improper VAV minimum airflow settings
  Exiting buildings could set VAV minimum airflows too high, so the VAV system normally runs as a CAV system
  Adjusting the deadband may need a proprietary software tools and can only be done by the building controls contractor
Method: Increase zone temperature setpoint by 2 Deg F

## Slide 27: Minimum Airflow Adjustment

## Slide 28: An Example
An ADR test day
  Simulated peak load event from 2 – 4pm
  RTU power dropped from ~30kW to ~20kW
  Rebound effect
  Trane VAV min. still not adjustable
Event start
Event end

## Slide 29: Lessons Learned and Future GEB Research/Demonstration
VOLTTRON
- Open source, cost effective
- Steep learning curve
Need to fix BAS issues first
Value proposition is key
Integration other DERs
Automated Demand Response
DER Optimization and Control
- Zone setpoint deadband
- VAV min. airflow adjustment
- Value to building owners
- Value to utilities
- Solar PV + battery storage
- EV charging
- OpenADR
- IEEE 2030.5
- Optimize and control all DERs
- Muti-objective optimization

## Slide 30: Questions and Discussion
Xiaohui “Joe” Zhou, PhD, PE, CEM
Director of Research and Innovation
jzhou@slipstreaminc.org